## Slide 1: MOSA: A Mobile Offloading Architecture using Software-defined network
Binh Nguyen and Junguk Cho
Mentors: Kobus Van der Merwe and Robert Ricci

## Slide 2: Outline
Motivation & related works.
Architecture.
Implementation.
Evaluation.
Conclusion.

## Slide 3: Motivation
Flat core design leads to a dominance of the Internet delay (the speed of light constraint).
Quality of service (QoS) requirement.
Inside the core: hierarchical routing issue.
Business model.
=> An approach that is able to “deeply” reduce the end-to-end delay.
Base station
(eNodeB)
Service gateway
(SGW)
Packet gateway
(PGW)
GameA
server
GTP
tunnel
GTP
tunnel
GTP
tunnel
Radio Access Network
(RAN)
Cellular core network
Internet
User device
(UE)
m.youtube.com
Delay reduces
dominated
End-to-end delay

## Slide 4: MOCA
Base station
(eNodeB)
Service gateway
(SGW)
Packet gateway
(PGW)
GameA
server
GTP
tunnel
GTP
tunnel
GTP
tunnel
Radio Access Network
(RAN)
Cellular core network
Internet
User device
(UE)
m.youtube.com
Local S-PGW instance
+ GameA server
MME
Offloading traffic by creating new tunnels to a local SPGW instance and server.
Modifying the control plane (Mobility Management Entity - MME) of the network
to realize the above goal.
An Architecture for Mobile Offloading using Cloud.

## Slide 5: MOSA
Base station
(eNodeB)
Service gateway
(SGW)
Packet gateway
(PGW)
GameA
server
GTP
tunnel
GTP
tunnel
GTP
tunnel
Radio Access Network
(RAN)
Cellular core network
Internet
User device
(UE)
m.youtube.com
Question: an offloading architecture using SDN without modifying the current components?
Only snooping the control plane is needed.
MME
GameA server
SDN substrate
(core network equivalence)

## Slide 6: Architecture overview
1
2
3
2
2
Ipv4
Tcp/udp
payload
Ipv4
Tcp/udp
payload
Ipv4
Udp
Gtp-u
Ipv4
Tcp/udp
payload
Ipv4
Tcp/udp
payload
Ipv4
Udp
Gtp-u